## Slide 1
Start
Store previous Hall encoder value
New Hall encoder value different than previous one
Increase repetition counter
Increase timeout counter
Timeout counter > timeout
End
yes
no
New value = 6
AND
Old value = 1
New value = 1
AND
Old value = 6
Restart
repetition counter
no
no
yes
yes
Electric speed
= (timer frequency)
x (repetition counter)
x (2 Pi)
Electric speed
= -(timer frequency)
x (repetition counter)
x (2 Pi)
Electric speed = 0
Electric speed
Electric speed =
previous electric speed
Read new Hall encoder value

## Slide 2
Start
Calculate Speed and update Hall encoder
New Hall encoder value different than previous one
OR
Speed < 5 rad/s
Dissable branch 3
Direction
Switch
(Hall encoder value)
Direction
1
Set
L1
Set complementary
PWM branch 2
Enable
outputs
1 and 2
Dissable branch 2
2
Set
L1
Set complementary
PWM branch 3
Enable
outputs
1 and 3
Dissable branch 1
6
Set
L3
Set complementary
PWM branch 2
Enable
outputs
2 and 3
…
Dissable branch 3
Switch
(Hall encoder value)
1
Set
L2
Set complementary
PWM branch 1
Enable
outputs
1 and 2
Dissable branch 2
2
Set
L3
Set complementary
PWM branch 1
Enable
outputs
1 and 3
Dissable branch 1
6
Set
L2
Set complementary
PWM branch 3
Enable
outputs
2 and 3
…
Counter-Clockwise
Clockwise
false
false
false
false
false
false
End
yes
no

## Slide 3
Start
Calculate speed
Get phase currents
Get bus voltage
Get angular position
Quadrature current,
Direct current
Clarke transform of measured currents
Park transform of α and β currents measured
Obtain quadrature voltage by
quadrature current PI control
using quadrature current measured
and quadrature current reference
Obtain direct voltage by
direct current PI control
using direct current measured
and direct current reference
Inverse Park transform of
quadrature and direct voltages
Inverse Park transform of
α and β voltages
Sinusoidal Drive
using A, B and C voltages
End

## Slide 4
Start
Miosix initialization
Run communications thread
Run motor control thread
Run status thread
Threads creation